ROCK LINED CHUTE QUANTITIES

Landuser:	 County:

Designed by:	 Date:	 Checked by:	 Date:

Rock Lined Chute Parameters:

Bottom Width (b):		b = 	 feet

Chute Flow Depth (d):	d = 	 feet

Controlled Drop (F):		F = 	 feet

Chute Profile Slope (S):	S = 	 :1

Chute Side Slopes (Z):		Z = 	 :1

Rock Size (d50):		d50 = 	 inches

Rock Lining Thickness (tr):		tr = 	 inches

Rock Density (Dr):		Dr = 	 pcf

Bedding Thickness (tb):		tb = 	 inches

Bedding Density (Db):		Db = 	 pcf

Volume of Rock:

Entrance Section:

de = 	 feet	Le = 	 feet	be = 	 feet

Upstream End Volume of Rock/Foot (at tr = 1’):

Vu = be + 2(de)(z2+1)0.5 +A*		Vu = 	 cf/ft

Downstream End Volume of Rock/Foot (at tr = 1’):

Vu = b + 2(de)(z2+1)0.5 +A*		Vd = 	 cf/ft

VE = (Vu + Vd) (0.5) (tr) (Le)		VE = 	 cu. ft.

Chute Section:

dc = 	 feet	Lc = 	 feet

Volume of Rock/Foot (at tr = 1’):

Vc = b + 2(dc)(z2+1)0.5 +A*		Vc = 	 cf/ft

VC = (Vc) (tr) (F) (S2+1)0.5		VC = 	 cu. ft.

Outlet Section:

do = 	 feet	Ld = 	 feet

Volume of Rock/Foot (at tr = 1’):

Vo = b + 2(do)(z2+1)0.5 +A*		Vo = 	 cf/ft

VO = (Vo) (tr) (Lo)		VO = 	 cu. ft.

Total Volume of Rock:

Vr = (VE) + (VC) + (VO)		Vr = 	 cu. ft.

Quantity of Rock:  (Vr) (Dr / 2000) = 			 tons

Volume of Bedding:

Vb = (Vr) (tb/tr)		Vb = 	 cu. ft.

Quantity of Bedding:  (Vb) (Db/2000) =			 tons

Quantity of Geotextile Fabric:

gf = (Vr)/(tr)		gf = 	 sq. ft.

Add 10% for laps, ends, waste, etc.

Geotextile fabric required: Gf = (1.1) (gf) = 		 sq. ft.

Gf (9 =				 sq. yd.

* correction for fill section (see EFM Figure IN-6-11)