## Slide 1: Decreasing hazards from non-point source pesticide contamination
Main ways to approach hazard reduction:
Manage pesticides differently
  reduced rate, delayed application, substitution
Manage crops differently
  crop rotation, planting dates, resistant varieties
Control off-site pesticide movement
  Buffers, Water management, Crop residue management

## Slide 2: Mitigating non-point source pesticide contamination
Typically mitigation measures:
Reduce pesticide application lbs/acre
Utilize less hazardous pesticides
Prevent pesticide from moving away from point of efficacy (in field)
Prevent pesticide from leaving field (bottom of root zone - edge of field)

## Slide 3: Reducing pesticide application:
NRCS does not “recommend” any pesticide, rate, formulation, or timing
All changes in pesticide management must be done with the help of Extension and crop consultants

## Slide 4: Reducing pesticide application:
Integrated Pest Management
  scouting
  apply only when economic threshold is reached
  use pest resistant varieties
  use good sanitation practices
  use crop rotation or delayed planting

## Slide 5: Reducing pesticide application:
Keep plants healthy and vigorous
Use lowest effective rate
Apply to part of the field
  banding
  spot treatment

## Slide 6: Reducing pesticide application:
Avoid treatments that rely mainly on residual activity for control
  early pre-plant
  fall application to control spring weeds
Use post-emergent treatments
Utilize directed sprays
Use lower application rate pesticides

## Slide 7: Reducing pesticide application:
Use mixtures of low rate pesticides instead of a single pesticide at a high rate
  Partial substitution
Proper maintenance and calibration of equipment

## Slide 8: Utilize pesticides that are less environmentally hazardous
NRCS can help determine at the field level
  Potential pesticide loss
  Potential pesticide hazard
NRCS does not make pesticide recommendations to producers
We can work with Extension or other crop advisors to help them include environmental risk in their recommendations

## Slide 9: Prevent pesticide from moving away from point of efficacy
Pesticides which move away from their target can no longer control the pest
  Soil Incorporation (decreases runoff)
  Use less mobile pesticides
  Adjuvants

## Slide 10: Prevent pesticide from moving away from point of efficacy
Decrease drift
  Adjusting spray equipment (droplet size)
  Don’t apply in windy conditions
Direct application toward target pest
  Avoid aerial applications or mist blowers
  Use wick applicators or other targeting technologies

## Slide 11: Prevent pesticide from moving away from point of efficacy
Use infield conservation techniques that
  Slow movement of water, chemicals and soil
  Trap sediment within the field
  Encourage infiltration within the field
Examples
  Residue Management
  Farming “across the slope”
  Farming “on the contour”
  Contour strip crops
  Contour buffer strips

## Slide 12: Prevent pesticide from moving away from point of efficacy
Avoid applying pesticide before a heavy rainfall
Practice efficient irrigation techniques
  Minimize leaching
  Minimize runoff
  Time pesticide application to coincide with irrigation
  Chemigate judiciously

## Slide 13: Prevent pesticide from moving away from point of efficacy
“Maintaining pesticide efficacy reduces overall use of pesticides, and off-target movement is less likely to occur”
From:
  Improved Pesticide Application BMPs for Groundwater Protection from Pesticides
  NDSU Extension Service, North Dakota State University

## Slide 14: Prevent pesticide from leaving field (bottom of root zone)
Practices that decrease leaching
  Use less pesticide
    economic threshold
    lowest effective rate
    lower rate pesticide
    Apply to less of the field (banding, spot treatment)
  Switch to less ‘leachable’ pesticide
    avoid using high leaching pesticide on high leaching soil

## Slide 15: Prevent pesticide from leaving field (bottom of root zone)
Practices that decrease leaching:
  Alter the ‘driver’
    avoid pesticide application before storms
    manage irrigation to prevent leaching (and run-off)
  Increase filtration
    increase soil organic matter
    disturb surface connected macropores
  Switch to less hazardous pesticide

## Slide 16: Prevent pesticide from leaving field (edge of field)
  Use less pesticide
    economic threshold
    lowest effective rate
    lower rate pesticide
    apply to less of the filed (banding, spot treatment)
  Soil incorporate
  Practices that increase infiltration
    On field
      residue management
      increasing soil organic matter

## Slide 17: Prevent pesticide from leaving field (bottom of root zone - edge of field)
  Practices that increase infiltration (continued)
    On field
      maintaining soil health
      tillage direction (contour)
      strip crops
      preventing/disturbing soil crusts
    Maintain sub-surface drainage

## Slide 18: Prevent pesticide from leaving field (edge of field)
  Catching pesticides at field edge
    buffer (filter) strips
    retention ponds
    constructed wetlands
    grassed waterways