# PEAK DISCHARGE COMPUTATION SHEET

## METHOD II

Owner        	 	Operator

SCD        	 	County

Practice        	  Location        	 ¼ of the       	¼ of Section     	, T.     	N, R.     	 W

- Given:	*Drainage Area (< 2000 Ac.)	(DA) =       	  Acres        	  Square Miles

Storm Type & Duration	Type         1	 ,        24     Hours

*Design Frequency	         =       	  Years,      	 % Chance

*Rainfall Depth	 (P)   =       	  Inches

*Average Watershed Slope	         =       	  %

*Runoff Curve No. (Present/Future) 	(CN) =       	  (See Table 3-1 or Table 3-2)

*Hydraulic Length	         =       	  Feet

- Obtain Runoff Depth  (From Table 3-5):  	R.O. Depth =      	  Inches

- Compute Watershed Lag  (Figure 5-11):    Watershed Lag  =      	  Hours

- **Impervious Area  (Figure 5-12):     (Future Condition – Urban Modification)

*% Impervious Area (IMP)  =      	 %

IMP Modification Factor      =

- **Hydraulic Length Modified:  (Figure 5-13):   (Future Condition – Urban Modification)

*% Hydr. Length Modified (HLM)  =        	 %

HLM Modification Factor                =

- Modify Watershed Lag:

##### Lag Mod.  =   Lag  (Hours)      x  IMP Mod. Factor   x  HLM Mod. Factor

Lag Mod.  =        	 Hours  x                  	      x

Lag Mod.  =        	 Hours

- Compute Time of Concentration (Tc):  Tc  =  1.67 x Lag  =        	 Hours

- Compute Basic Discharge (CFS):

From Figure 5-1 Select Hydrograph Family

#### From Figure 5-2 Select CSM Rate                         	 CSM

QB  =  DA  (Square Miles)    x  Inches R.O.  x  CSM Rate

QB  =                 	             x           	        x

QB  =                 	  CFS

- Ponding & Swamp Storage Adjustment  (Tables 5-1, 5-2, 5-3):

*% of Ponding and Swampy Area =     	 % (Based on Actual DA)

*Location in Watershed (check one):   Design Point     	;  Center     	;  Upper     	.

Ponding Adjustment Factor =

- Modify Discharge For Ponding & Swamp Storage:

#### QMOD  =      QB      x       Ponding Adj. Factor

QMOD   =       	  x       	  =        	 CFS

*Input Data  **Optional Adjustments.  If the Adjustment is not used, the Factor = 1.0

Referenced Figures, Tables, and Example Problems are Contained in the Hydrology Manual for

North Dakota, Chapter 5.

Computed by        	   Date

Checked by        	   Date